## Slide 1: REAL-TIME CHESS GAME ANALYZER
Serden Sait Eranil
Veysel Colak
Firdevs Su Aydin

## Slide 2: Outline
Motivation
Project Steps & Work Distribution
Project Pipeline (ROS Nodes & Topics)
Deeper Look Into Project Steps
Accuracy and Delay Results
Demo
Future Scope

## Slide 3: Motivation
Automate recording of the moves
Instead understand the moves with camera and save them

## Slide 4: Project Steps & Work Distribution
Data Collection & Annotation | YOLO Model Selection | Piece, Checkerboard and Hand Detection
Serden Su Veysel | Su Serden | Su Serden
Game State Management | Visualization | ROS Pipeline & Workspace
Veysel | Serden | Veysel

## Slide 5: Project Pipeline (ROS Nodes & Topics)

## Slide 6
Deeper Look Into Project Steps

## Slide 7: ROS
Robot Operating System is...
  a robotics workframe.
  a library for C and Python.
  a middleware between distributed system.
"Nodes", "Topics", "Services", "Actions" ...
Notes: Minimal modules called "nodes".
"Nodes" can communicate via streams called "topics". Nodes can "publish" or "subscribe"
"Nodes" have "services" and "actions" for client/server type interactions

## Slide 8: What does ROS bring?
The "communicating nodes" structure
In robotics domain also...
Notes: of ROS enables to use different nodes on different devices independently.
Standardization of robotics development
High-Level / Low level abstraction

## Slide 9: But there are two of them!
ROS has two versions: ROS & ROS2.
  No Masters
  Message QoS profiling
Due to lab computers and bag files,
we have moved our project to ROS1
Notes: Also: EOL, Aggressive Patches, Microsoft/MacOs...

## Slide 10: ROS Implementation (with Camera Node)

## Slide 11: ROS Implementation (with Test Node)
Utilize the ROS node2node communication
On parallel use a "~perfectly arranged determiner"
  Use the branch for each step after "/im" topic

## Slide 12: ROS Reading Camera (/ros2im)
Other nodes subscribe 1 topic
  But /ros2im subscribes 2 topics
  They should be combined.
Approximate Time Synchroniser

## Slide 13: Time Synchronization in ROS
TimeSynchronizer:
  Perfect but Unimplementable
ApproximateTimeSynchronizer:
  Frame loss possible but works

## Slide 14
DATA ANNOTATION
TRAINING AND TEST

## Slide 15: Data Collection and Annotation
8 Recordings
4 Cameras: 2 top views, 2 side views

## Slide 16: Data Collection and Annotation
Training Dataset:
6 recordings, 4 cameras
Total of 132 training
images
Records 1 to 6
Top View1
Top View2
Side View1
Side View2
4 Images
7 Images
7 Images
4 Images

## Slide 17: Data Collection and Annotation
Validation Dataset:
1 recording, 2 top views
Total of 20 validation
  images
Test Dataset:
1 recording, 2 top views
Total of 20 test
  images
Record 7
Top View1
Top View2
10 Images
10 Images
Record 8
Top View1
Top View2
10 Images
10 Images

## Slide 18: Data Collection and Annotation
Data Distribution:
12 piece + hand + checkerboard
Not evenly distributed

## Slide 19: CVAT: Computer Vision Annotation Tool
Easy-to-use, open-source, collaborative web-based tool
Allows the use of state-of-the-art segmentation methods (e.g., Segment Anything, HRNET)

## Slide 20: Why didn't we use MIVOS?
Poor quality of the pieces
Insufficient support of instances
Fast hand movements
Too chaotic piece distribution
Solution: Through use of CVAT, add some manual input

## Slide 21: How did we do the annotation in CVAT: GIF

## Slide 22: Final annotation outcome per frame

## Slide 23
YOLO MODELS

## Slide 24: YOLO Model Selection
4 sizes of YOLO v8 model:
    Nano
    Small
    Medium
    Large
Figure: Parameters of YOLO models. Adapted from https://github.com/ultralytics/ultralytics

## Slide 25: YOLO Model Selection
Figure2: Training curves for medium model.
Figure1: Training curves for small model.
Training:
Avoid overfitting.

## Slide 26: YOLO Model Selection
Test: Confusion matrices
Some pieces are confused with each other.
Figure 1: Confusion matrix for large model with test data
Figure 2: Confusion matrix for small model with test data

## Slide 27: YOLO Model Selection
Test: F1 Scores​
Kings and Queens are harder to detect.
Figure: F1 Score of medium model

## Slide 28: YOLO Model Selection
Test: F1 Scores
Confidence threshold is determined by F1 Score.
Medium model is selected.
Model | Max F1 S. | Confidence
Nano | 0.81 | 0.374
Small | 0.89 | 0.553
Medium | 0.91 | 0.384
Large | 0.93 | 0.274

## Slide 29: YOLO Model Selection
Some detection examples: Only pawns

## Slide 30: YOLO Model Selection
Some detection examples: Rooks and Bishops

## Slide 31: YOLO Model Selection
Some detection examples: Knights, Kings and Queens

## Slide 32: YOLO Model Selection
Some detection examples: Checkerboard and Hands

## Slide 33: YOLO Model Selection
Detection Challenges:
White bishops are hard to detect.
Queens and kings are sometimes confused for each other.
Figure 2: Undetected white bishop
Figure 1: Wrongly detected white queen

## Slide 34: Piece, Checkerboard and Hand Detection

## Slide 35: Piece, Checkerboard and Hand Detection
Frame(s)
Checkerboard coordinates
Hand flag
Piece classes
Piece bounding boxes
Piece probabilities

## Slide 36: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 37: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 38: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 39: Checkerboard Corner Detection​
Hough-Line Transform:
        Point -> Sinusoid
        Intersection of sinusoids means line
Hough Transform
Figure 1: Line on image domain. Adapted from https://shorturl.at/lBOX5
Figure 2: Sinusoids on image domain. Adapted from https://shorturl.at/lBOX5

## Slide 40: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 41: Harris Corner Detection: Basic Idea
Figure: Harris Corner Detection. Adapted from https://shorturl.at/jtwQ8

## Slide 42: Harris Corner Detection: Good for chess

## Slide 43: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 44: Checkerboard Corner Detection
What if some corners are not detected? Or some corners are wrongly detected?

## Slide 45: Checkerboard Corner Detection​
Predict vertical and horizontal edge vectors.
Median of existing vertical and horizontal vectors.

## Slide 46: Checkerboard Corner Detection
For excess corners
If detected corner does not match with any of predicted corners, delete the corner.
Look at detected corner locations

## Slide 47: Checkerboard Corner Detection
For missing corners
Look at expected corner locations.
If corner exists pass, if corner does not exist add a corner.

## Slide 48: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 49: Checkerboard Corner Detection
Checkerboard Frame
Canny Edge Detection
Hough Line Transform
Harris Corner Detection
Correct Corners
Sorted corner coordinates
Sorting

## Slide 50: Piece Detection
Yolo Model
Frame
Piece classes
Piece bounding boxes
Piece probabilities

## Slide 51: Hand Detection: Intersection Over Union
Hand Flag =
1 if IoU > threshold
0 otherwise

## Slide 52: Intersection over Hand (IoH)
To understand what ratio of hand is over the checkerboard

## Slide 53
GAME STATE

## Slide 54: Game State Management

## Slide 55: Game State Management
Chessboard
Checkerboard coordinates
Hand flag
Piece classes
Piece bounding boxes
Piece probabilities
Player/Playing?

## Slide 56: Game State Management – State Machine

## Slide 57: Game State Management
Read the board only at the end of a move!
The reasons for the decision:
  Avoid piece detection errors due to blockage of hand
  Fasten the code

## Slide 58: Placing the Pieces into the Chessboard
We should evaluate the BBox and Checkerboard corners in order to determine the state of the board.
The implementation differs for single and multicamera scenarios.

## Slide 59: Chessboard Placement – Single Camera

## Slide 60: Chessboard Placement – Multicamera

## Slide 61
VISUALIZATION

## Slide 62: Real-time visualization with Tkinter
Visualization (Ros Node)
Visualization Script
Visualization Thread
Puts pieces on board
Visualization is a subprocess.
Send game state to subprocess through open pipe.
Thread checks if data is on pipe and draws it.
Run in infinite loop

## Slide 63: Real-time tracking of remaining times.

## Slide 64: Hand State on Title
4 State: P2s Move, P1s Move, P1s Hand on the board, P2s Hand on the board
Updated in the Tkinter window in real-time

## Slide 65: Hand State on Title
4 State: P2s Move, P1s Move, P1s Hand on the board, P2s Hand on the board
Updated in the Tkinter window in real-time

## Slide 66
PERFORMANCE COMPARISIONS

## Slide 67: Accuracy calculation on run-time
Use a perfect YOLO model
  Every piece is correctly classified
  Now we can test accuracy by frame

## Slide 68: Confusion Matrix for overfitted model

## Slide 69: Accuracy Results for YoloV8n (nano)
From 0.92 to 0.94 with the cost of delay
Mean performance is 0.9219

## Slide 70: Accuracy Results for YoloV8s (small)
Single camera accuracy moved to 0.95 from 0.92 (YoloV8n)
Multi camera accuracy moved to 0.98 from 0.94 (YoloV8n)

## Slide 71: Accuracy Results for YoloV8m (medium)
Single camera accuracy moved to 0.98 from 0.95 (YoloV8s)
Multi camera accuracy moved to 0.9875 from 0.9808 (YoloV8s)

## Slide 72: Accuracy Results for YoloV8l (large)
Single camera accuracy moved to 0.97 from 0.98 (YoloV8m)
Multi camera accuracy moved to 0.9754 rom 0.9875 (YoloV8m)
Large model performs worse since we don't have enough data

## Slide 73: Multi-view Camera: does it pay off?
It brings a marginal improvement over accuracy.
However, we need to detect corners at the beginning two times
Also with initialization, first delay is higher.

## Slide 74: Multi-view Camera: stable after first frame
After initialization, it processes the frames in comparable times
Since medium model has more parameter, it takes more time to compute prediction than that of the small model

## Slide 75: Delay: Multi vs. Single-Camera
Second camera is sequentially processed with the first one
That causes the delay to almost double for every node
Timings are given for small model

## Slide 76: Delay: Multi vs. Single-Camera
Second camera is sequentially processed with the first one
That causes the delay to almost double for every node
Timings are given for medium model (increased w.r.t. to small)

## Slide 77: The trade-off of speed and accuracy

## Slide 78: DEMO: YoloV8m, MultiCamera

## Slide 79: DEMO: YoloV8m, SingleCamera

## Slide 80: DEMO: Single Camera with Ground Truth

## Slide 81: FUTURE WORK
One node creates too much delay comparatively
Buffer of /im topic can become unstabilized
  Suggestion: Re-arrange the node-topic pipeline for app. eq. Delays
  Challenge: Each code snippet should be taken into account

## Slide 82: References
https://wiki.ros.org/message_filters/ApproximateTime
https://wiki.ros.org/message_filters#Overview
https://roboticsbackend.com/ros1-vs-ros2-practical-overview/
https://roboticsbackend.com/what-is-ros/
https://github.com/ultralytics/ultralytics
https://docs.opencv.org/3.4/dc/d0d/tutorial_py_features_harris.html
https://docs.opencv.org/3.4/d9/db0/tutorial_hough_lines.html

## Slide 83
QUESTIONS